BOLT

Technical Specifications

| Fuel Type | Gasoline | Diesel |
| --- | --- | --- |
| Engine | Revotron 1.2T | 1.3L Quadrajet |
| Max. Engine Output | 63 kW @ 5000 rpm | 55 kW @ 4000 rpm |
| Max. Torque | 140 Nm @1750-3500 rpm | 190 Nm @1750- 3000 rpm |
| Gearbox | TA65* | C510 |
| Steering | Electronic power steering with brushless motor |
| Wheelbase (mm) | 2470 |
| Length x Width x Height (mm) | 3825 x 1695 x 1550 |
| Wheel Track (mm) | Front: 1450 Rear: 1440 |
| Kerb Weight (Kg) | 1080 |
| Payload (Kg) | 425 |
| Brakes | Vacuum Assisted Independent Hydraulic; Front: Ventilated Disc Brakes. Rear: Drum Brakes |
| Clutch | Dry Single Plate |
| Suspension | Front: Dual Path Independent McPherson strut with Anti-roll Bar Rear: Independent 3- link Mc Pherson strut with Anti-roll Bar |
| Fuel Tank Capacity (Litres) | 44 |

Standard / Optional Features

DesigNext

- New Tata grille visually flowing into the dynamic headlamps

- Floating roof spoiler aids sporty touch and aerodynamics

- Strong shoulder lines, new front identity imparting a wider stance

- Darkened C-pillar creates a distinctive floating roof design

- Premium chrome finish on Dashboard

DriveNext

- Revotron 1.2T – New Turbocharged Intercooled MPFI Engine

- Economy / sport / normal mode

- Electronic power steering with ‘Active Return’

ConnectNext

- HARMAN infotainment system

- 5-inch touchscreen supporting rich multimedia experience

- Advanced Bluetooth technology

- Smart voice recognition

- Advanced smartphone integration supporting phone enabled navigaton

- Social media integration

- HVAC controls through the infotainment system